## Slide 1
Robot Cognition
Team Toucan
Conceptual Design Report
Sponsor: Bill Michael
Faculty Sponsor: Leslie Tekamp
10-7-2022

## Slide 2: Contents
Problem Specification
Hardware Integration
Platform Structure Design

## Slide 3: Problem Specification
The goal of this project is to create a platform that can incorporate sensors to allow for the mapping of its surrounding area.
  Sensors that will be used are:
    GPS
    Inertial Measurement Unit (IMU)
    LIDAR
    Camera
  The platform must weigh less than 5kg
  Formats data into a single processing system

## Slide 4: Problem Specification
The platform must also provide additional ports:
  5VDC at 10A
  3.3VDC at 10A
  12VDC at 5A
Must be fully functional from –10o to 40o C

## Slide 5: Major Hardware
Processor: NVIDIA Jetson Nano
Integrate the following onto one platform:
  Xsens MTI-10-2A8G4 (Inertial measurement unit)
  Ublox LEA-M8T with WD22UGRC interface board (Global positioning system)
  Velodyne LiDAR PUCK 16 (LIDAR)
  e-CAM24_CUNX (Camera)
  Need to consider a power source

## Slide 6: NVIDIA Jetson Nano
GPU | 128-core NVIDIA Maxwell™
CPU | Quad-core ARM® A57 @ 1.43 GHz
Memory | 2 GB 64-bit LPDDR4 25.6 GB/s
Storage | microSD
Video Encode | 4Kp30 ¦ 4x 1080p30 ¦ 9x 720p30 (H.264/H.265)
Video Decode | 4Kp60 ¦ 2x 4Kp30 ¦ 8x 1080p30 ¦ 18x 720p30 (H.264/H.265)
Connectivity | Gigabit Ethernet, 802.11ac wireless
Camera | 1x MIPI CSI-2 connector
Display | HDMI
USB | 1x USB 3.0 Type A,2x USB 2.0 Type A, USB 2.0 Micro-B
Others | 40-pin header (GPIO, I2C, I2S, SPI, UART) 12-pin header (Power and related signals, UART) 4-pin Fan header

## Slide 7: IMU Integration
CA-MP2-MTI
CA-USB-MTI
Xsens MTI-10-2A8G4
Currently have CA-MP2-MTI
  Serial connector
Alternative CA-USB-MTI
  Allow for easier integration with USB

## Slide 8: IMU Alternative
Xsens MTI-OEM
UART Communication Protocol
  Provides flexibility if we run into integration issues

## Slide 9: GPS Integration
Ublox LEA-M8T
SPI (serial peripheral interface)
UART
I2C (inter-integrated circuit) communication protocols
Plan to use UART communication protocol
Needs to be integrated with an Antenna

## Slide 10: LIDAR Integration
Velodyne LiDAR PUCK 16
Ethernet Communication protocol

## Slide 11: Camera Integration
e-CAM24_CUNX
MIPI camera serial interface 2 (CSI-2) communication protocol
  Connects directly to Jetson Nano

## Slide 12: Design Ideas
Idea #1
Platform:
Compact
2-3 Levels
Convenient Mounting points
Open layout
(Not closed on sides)

## Slide 13: Design Ideas
Idea #2
Mobility:
2 large powered tires + 1 small (stability)
v.s 4 tires on a solid chassis.
Convenient Mounting points
Open layout (Not closed on sides)
Consumables, budget, variables (speed, power cap..),
Feature Creep, design complexity and deadlines, etc..

## Slide 14: Design Ideas
Idea #3
One platform
  Lower center of gravity (more stable)
  3D printed custom platform
Jetson Nano
Extra ports
IMU
GPS
LIDAR
Camera
Front
Antenna

## Slide 15: Problem Requirements
Requirement: A sensor platform to be built that is capable of taking information from the surrounding area and processing for a cognition robot.
Requirement​ | ​
Power Supply​ | 18-48V​
Peripherals​ | GPS, IMU, LIDAR, Camera​
Power Output ​ | 5VDC at 10A​
Power Output​ | 3.3VDC at 10A​
Power Output​ | 12VDC at 5A​
Generates​ | Point-cloud data, spatial and image data, location data​
Collects ​ | Accurate geo positioning, image and video collection, attitude and gyroscope data, inertial data​

## Slide 16: Comparison of Solution Concepts to Problem Requirements and Decision Matrix
Requirement | Design 1 (Multiplatform) | Design 2 | Design 3 (Single platform)
Capable of taking in information | Provides camera and LIDAR with full view 10 |  | Objects intersecting view of camera and LIDAR 5

## Slide 17: Concept Recommendation
Recommend design idea 1

## Slide 18: Bill of Materials
Item | Unit | Quantity | Total | Manufacturer | Description
e-CAM24_CUNX | $154.00 | 1 | $154.00 | E-con Systems | Camera
NVIDIA Jetson Nano | $59.00 | 1 | $59.00 | Nvidia | processing unit
Velodyne LIDAR PUCK 16 | $4,000.00 | 1 | $4,000.00 | Velodyne | LIDAR
Xsens MTI-10-2A8G4 | $759.00 | 1 | $759.00 | Xsens | IMU
Ublox LEA-M8T | $89.00 | 1 | $89.00 | U-blox | GPS
3D Print Platform | ? | 1 | ? |  | 
Total |  |  | $5061.00 |  | 

## Slide 19: Plan to Complete Design (Deadlines)
September 16: Conceptual Design Report
October 7: Critical Design Documents
October 14: Finish sensor integration
November 11: Finish software integration
December 2: Final Report