## Slide 1
Robot Cognition
Team Toucan
Critical Design Review
Sponsor: Bill Michael
Faculty Sponsor: Leslie Tekamp
10-7-2022

## Slide 2: Contents
Description of Design
Design Drawings
Electrical Connections
Test Plan
Software Design Plan

## Slide 3: Design Description
The goal of this project is to create a platform that can incorporate sensors to allow for the mapping of its surrounding area.
  Sensors that will be used are:
    GPS
    Inertial Measurement Unit (IMU)
    LIDAR
    Camera
  The platform must weigh less than 5kg
  Formats data into a single processing system

## Slide 4: Major Hardware
Processor: NVIDIA Jetson Nano
Integrate the following onto one platform:
  Xsens MTI-10-2A8G4 (Inertial measurement unit)
  Ublox LEA-M8T with WD22UGRC interface board (Global positioning system)
  Velodyne LiDAR PUCK 16 (LIDAR)
  e-CAM24_CUNX (Camera)
  18-36V LIPO battery

## Slide 5: Component Weights
Total Component Weight | 
Item | Weight (g)
LIDAR | 849
GPS + Antenna | 97
NANO | 269
Camera | 37
Cased IMU | 56
Total | 1308
Weights do not include cables
3.69 kg remaining

## Slide 6: 3D Model

## Slide 7: 3D Model cont.

## Slide 8: Design Drawings

## Slide 9: Design Drawings cont.

## Slide 10: Electrical Connections

## Slide 11: DC/DC Isolated Converters

## Slide 12: To meet Class B compliance for EN55032

## Slide 13: Provides Power to Jetson Nano

## Slide 14: Provides Power to Lidar

## Slide 15: Provides Power to Three Additional Ports

## Slide 16: Power Connections
Point A | Point B | # of Connection | Connector
Battery | Wire A (6 AWG) | 2 | EC5
Wire A | CP40B Externals | 6 | Soldered 12 AWG Wire
Wire A | PQAE50 Externals | 2 | Soldered 12 AWG Wire
Wire A | RSDW60G Externals | 2 | Soldered 12 AWG Wire
CP40B Externals | CP40B DC/DC | 6 | Wire Pin Terminal
PQAE50 Externals | PQAE50 DC/DC | 4 | Wire Pin Terminal
RSDW60G Externals | RSDW60G DC/DC | 4 | Wire Pin Terminal
CP40B DC/DC (5V) | Jetson Nano | 2 | Wire Pin Terminal
CP40B DC/DC (12V) | LIDAR | 2 | Soldered 12 AWG Wire
CP40B DC/DC (3.3V) | Port A | 2 | Female to Male Pin Connector
PQAE50 DC/DC (5V) | Port B | 2 | Female to Male Pin Connector
RSDW60G DC/DC (12V) | Port C | 2 | Female to Male Pin Connector

## Slide 17: Signal Connections
Point A | Point B | # of Connections | Connector
Jetson Nano | LIDAR | 1 | Ethernet
Jetson Nano | LEA-M8T (GPS) | 3 | UART
Jetson Nano | Xsens MTI-10-2A8G4 (IMU) | 1 | USB
Jetson Nano | e-CAM24_CUNX​ (Camera) | 1 | MIPI CSI-2
LEA-M8T | Antenna | 1 | SMB to TNC Coax

## Slide 18: Software Design Plan Introduction
Installation of required Software and interfaces
Building Code and testbenches for interfacing with the I/O components Through their drivers
Learning how to use the TensorRT interfaced through python/C++ for image recognition
Building Code for the robot to perform all customer requirements
Further testing for bugs, quality control of software.
Schedule and deadlines

## Slide 19: SDP: Installation of required Software and interfaces
Installation of runtime libraries
Installation of c++, python libraries
Interfaces for python,C++ to interface with TensorRT on the jetson nano
Installation of All I/O Drivers for the I/O components

## Slide 20: SDP: Learning how to use the TensorRT interfaced through python/C++ for image recognition
Learning the libraries for python and C++
Writing the first program to run the inference of an image through TensorRT
Testing the percentages of accuracy for different detected objects, ensuring Hardware/Software cohesion
Testing different images with the recognition on the jetson nano with pre trained networks
Building a custom network for the specified customer requirements if needed

## Slide 21: Building Code for the robot to perform all customer requirements
Code to Deal with Datapaths (all inputs from I/O Components such as Lidar and Camera)
Code for the controller for navigation, states, and decision making.
Testing in various environments

## Slide 22: Test Plan Introduction
Testing is required to ensure that all the individual components are working properly in addition the components all working together properly
Tests ensure that the:
  GPS captures accurate positioning data at all locations
  IMU captures correct inertial and velocity in all instances
  LIDAR and camera captures correct imaging data in any space

## Slide 23: Test Plan Methodology and Procedure: GPS
Upon integration, the GPS will be taken to several locations to read coordinates
The coordinates read from the GPS will be compared to coordinates found on Google Maps.
A successful result will yield GPS coordinates within 10 meters of the actual location
An unsuccessful result will yield GPS coordinates that are more than 10 meters away from the actual location

## Slide 24: Test Plan Methodology and Procedure: IMU
Upon integration, the IMU will be turned in different ways (ex. Upside down, a 30° angle, 175° angle), taken to different altitudes (ex. Colorado Springs, Denver, Pikes Peak), and moved at different speeds (driven in a car)
Captured data will be analyzed
A successful result will show correct measurement for all attitudes, altitudes, and velocity
An unsuccessful result will be if the measurements do not match the expected values

## Slide 25: Test Plan and Methodology: LIDAR and Camera
Upon integration, the LIDAR and camera will be taken to different environments (ex. Classroom, open field, parking lot) to capture imaging data
A successful result of the tests will show the LIDAR and camera accurately imaging each space
An unsuccessful result of the tests will show the LIDAR and camera inaccurately imaging each space

## Slide 26: Test Plan Results and Analysis: GPS
Collected data: Coordinate data
Data was chosen because the purpose of the GPS is to provide positional data in the form of longitude and latitude coordinates
The collected data will be compared to data from Google Maps to ensure correctness

## Slide 27: Test Plan Results and Analysis: IMU
Collected data: attitude (angle), distance from sea level (meters), and velocity (meters per second)
Data was chosen so that each capability of the IMU can be verified
This data will be compared to manually collected data from Google Maps or attitude readers to ensure correctness

## Slide 28: Test Plan Results and Analysis: LIDAR and Camera
Collected data: Visual Imaging
Data was chosen because the purpose of the LIDAR and camera is to provide visuals
The collected data will be compared to team members’ observations of the space to ensure correctness

## Slide 29: Bill of Materials
Item | Unit | Quantity | Total | Manufacturer | Description
e-CAM24_CUNX | $154.00 | 1 | $154.00 | e-con Systems | Camera
NVIDIA Jetson Nano | $259.00 | 1 | $259.00 | NVIDIA | processing unit
Velodyne LIDAR PUCK 16 | $4,000.00 | 1 | $4,000.00 | Velodyne LIDAR | LIDAR
MTI-10-2A8G4 | $759.00 | 1 | $759.00 | Xsens | IMU
LEA-M8T | $89.00 | 1 | $89.00 | Ublox | GPS
3D Print Platform |  | 1 |  |  | 
HDMI Cable |  | 1 |  |  | 
CP40B_1790018 | $26.47 | 1 | $26.47 | Semiconductor Circuits Inc | DC/DC converter
CP40B_1180018 | $26.47 | 1 | $26.47 | Semiconductor Circuits Inc | DC/DC converter
CP40B_1233036 | $28.60 | 1 | $28.60 | Semiconductor Circuits Inc | DC/DC converter
PQAE50-D24-S5-D | $37.57 | 1 | $37.57 | CUI Inc | DC/DC converter
RSDW60G-12 | $63.77 | 1 | $63.77 | Mean Well | DC/DC converter
CA-USB-MTI | $68.00 | 1 | $68.00 | Xsens | IMU Connector
Misc Wires |  |  |  |  | 
Total | $5,511.88 |  |  |  | 

## Slide 30
Questions?